## Slide 1: Aerodynamics
Aerodynamic Device Overview
0.1 Why aero devices were adopted
Aero devices were introduced to achieve sharper vehicle behavior.
Simulation showed that downforce gains outweigh the added weight.
The team also had enough members and prior production tests to support development.
0.2 Development targets
1. Easy-to-manufacture geometry.
2. Sufficient downforce.
3. Strength against failure.
4. Weight reduction while prioritizing manufacturability.
0.3 Risk management
Because this was the first aero package, development was managed so it would not disrupt the full vehicle schedule.
If SES approval was delayed or a critical issue occurred, aero development would be stopped immediately.
0.4 Performance and production strategy
The tire-force plot shows vertical load on the horizontal axis and resultant tire force on the vertical axis.
Maximum tire force increases almost linearly with vertical load, so the design prioritizes downforce.
Manufacturing tests confirmed wet layup, VaRTM, demolding, vacuum quality, and cure-time requirements.
almost linear increase
Fig. 1 Vertical load vs. resultant tire force

## Slide 2: Aerodynamics
Rear Wing
The design process is summarized below.
1. Select airfoils and angles of attack
2. Determine slot gaps and overlaps
3. Build the 3D model
1. Airfoil selection and angle of attack
The rear wing was designed around S1223 because it has a high lift coefficient and strong low-Reynolds-number performance.
For a 3-element wing with a 1000 mm span, repeated 2D Ansys analyses showed that 0°, 30°, and 50° produced high downforce with low drag.
To reduce structural load and downforce instability from a large negative pitching moment, the main plane was changed from S1223 to S1223 RTL.
An upper wing was added to increase downforce.
The first upper element tended to stall, so E423 was selected.
NACA M3 was also checked, but with the small second-element angle there was little difference in separation or drag; E423 was better for downforce.
M = ・S・c・Cm (1)
：Dynamic pressure (N/m)
S：Representative area (m²)
C：Wingspan (m)
Cm： Pitching moment coefficient
The pitching moment coefficient was reduced from about -0.24 to about -0.10.
This cuts pitching moment by approximately 58%, improving structural and dynamic stability.

## Slide 3: Aerodynamics
2. Slot gaps and overlaps
After fixing the airfoils and angles of attack, 2D Ansys analyses were repeated while changing only slot gap and overlap.
The final airfoil layout, gap, and overlap values are shown in Fig. 1, and the final 2D result is shown in Fig. 2.
3. 3D modeling
The 3D model was built from the 2D results.
Considering the 1335 mm tread, approximately 200 mm tire width, weight, and manufacturing tolerance, the span was set to 1040 mm.
Wind speed: 40 km/h
Downforce: 159 N Drag: 4.9 N Span: 1000 mm
Image is vertically inverted for analysis.
Figure 1
Figure 2
Swanneck
stay
Strut placement was also optimized.
From the side, the swan neck and stay form a triangular structure; from the rear, the stays form a V shape.
This reduces part count while maintaining geometric stiffness.

## Slide 4
Aerodynamics
Front Wing
Target setting, design choices, and evaluation in one loop
1. Target / constraints
Use different element counts inside and outside the tire-front regulated area.
Target: span 1 m, wind speed 11 m/s (= 39.6 km/h), downforce >= 130 N.
Design aim: increase Df while minimizing drag; rear:front aero balance guideline = 4:6.
2. Solution / iteration
2D and 3D Ansys analyses measured Df and drag; SolidWorks Flow Simulation checked local airflow.
S1223 was the base low-Re airfoil, but 80 mm ride height limited ground effect.
The first tire-front (1) and inboard (2) elements were changed to E423 to suppress drag increase.
3. Evaluation / final result
Configuration checks: 129.08 N / 23.00 N drag and 110.76 N / 20.83 N drag.
Final evaluated result at span 1 m and 11 m/s: Df = -122 N, drag = 23.7183 N.
Ribs secure wing strength; the FB-lower section is flat to avoid IA/frame interference in collision.
Regulation concept
Airfoil / structure
Config. 1
Df 129.08 N / drag 23.00 N
Config. 2
Df 110.76 N / drag 20.83 N
Final position table
Conclusion
The front wing target was set from a 130 N downforce requirement at 1 m span and 11 m/s. The design was solved by iterating element count, airfoil choice, and wing position under regulation constraints, then evaluated by Df/drag analysis and manufacturability/impact-clearance checks.

## Slide 5: Aerodynamics
Floor
<Last year>
Purpose: driver protection
Material: glass mat
<This year>
Purpose: 1. driver protection
2. increase wheel load
→ diffuser added
Material: AFRP
Vehicle concept: “Strong, Sharp, Reliable”
For sharp cornering
- From “protection only” to “load generation”
- Provide stable downforce
For reliable operation
- Protect the radiator
- Select suitable mold method
- Select suitable material
Diffuser angle selection
Packaging around the powertrain limited the diffuser angle, so 5°, 10°, and 15° models were analyzed in 3D.
Ride height was varied from 10 to 50 mm in 10 mm steps to evaluate downforce stability during vertical vehicle motion.
The final angle was selected by prioritizing the largest minimum-to-maximum downforce ratio.
Analysis tool: OpenFOAM Flow speed: 11 m/s (= 40 km/h)
5°
15°
10°